## Slide 1: Unit 4, Lesson 11 Motherboards and Their Components
AOIT
Computer Systems
Copyright © 2008–2013 National Academy Foundation. All rights reserved.

## Slide 2: Motherboard designs differ by manufacturer
All motherboards have:
  Processor socket
  Memory and expansion card slots
  Power supply and hard drive connectors
  BIOS chip
  CMOS battery
Location on the board and quantities might vary.
Memory slots
Processor socket
Expansion card slots
Parallel port
Hard drive connector
CMOS battery

## Slide 3: Motherboards have slots and sockets
Slots hold expansion cards.
Sockets hold processors.
Empty slots
Processor in its socket
Copper traces carry data

## Slide 4: The CPU socket determines the kind of processor
Sockets are designed to make replacing the processor easy.
The pins on the processor must match the grid on the socket.
The processor must be compatible with the motherboard.
Can you tell which one is an LGA socket and which one is a PGA socket?
Notes: LGA image retrieved from http://en.wikipedia.org/wiki/File:CPU_Socket_775_T.jpg and reproduced here under the terms of the Creative Commons Attribution-ShareAlike 3.0 Unported license (http://creativecommons.org/licenses/by-sa/3.0/deed.en). Image courtesy of Appaloosa. PGA image retrieved from http://en.wikipedia.org/wiki/File:Intel_Socket_370.JPG and reproduced here under the terms of the Creative Commons Attribution-ShareAlike 3.0 Unported license. Image courtesy of Xeper.

## Slide 5: The processor is the brain of the computer
The processor, or CPU:
  Controls all computer functions
  Processes billions of instructions
  Performs math calculations
  Facilitates communication among components

## Slide 6: The motherboard chipset controls data transfer
The chipset:
  Directs data flow between system buses and peripherals
  Manages data transfer between the processor and memory
  Enables components to communicate with each other directly
  Manages bandwidth to ensure the processor tends to all components

## Slide 7: The front-side bus connects the processor to the north bridge
  The front-side bus connects the processor to other components by carrying data between the processor and north bridge.
  The north bridge then links data traffic from the processor to RAM.
Why do you think it is called the front-side bus?

## Slide 8: The system clock synchronizes the tasks a computer performs
The clock emits electrical pulses; each pulse is exactly one clock cycle.
The CPU performs one operation during each clock cycle.
Processor speed is measured in clock cycles per second, expressed in MHz or GHz.
The system clock synchronizes data transfer among the subsystems.

## Slide 9: Expansion cards provide additional features
Types of expansion cards:
  Graphics accelerators
  Video adapters
  Sound cards
  Internal modems
  Accelerator boards
  LAN cards
Although many computers have less expensive, lower quality versions of these components integrated onto the motherboard, you can install cards into the available slots for better quality sound or video.
LAN card

## Slide 10: PCIe is the standard for expansion cards
PCIe slots
PCIe slots
Slot designations describe how many lanes of data slots carry between the motherboard and a PCIe expansion card.
PCIe x1, x2, x4, x8, and x16 cards carry 1, 2, 4, 8, and 16 lanes of data.

## Slide 11: Power supply connectors provide power
The P4 ATX12V power connector plugs into a four-pin slot.
The P1 power connector has 24 pins.
Can you see the name of this connector printed on the motherboard?

## Slide 12: Hard drives connect to the motherboard
One end of the cable inserts into the back of the drive.
The other end inserts into a connector on the motherboard.
The cable has a red line running down one edge of it.
Notes: Image on this slide retrieved from http://www.easeus.com/resource/install-sata-hard-drive.htm and reproduced here under fair-use guidelines of Title 17, U.S. Code. Image courtesy of CHENGDU Yiwo Tech Development Co., Ltd

## Slide 13: Memory modules insert into RAM slots
RAM can be DIMMs or SIMMs.
Latches hold the memory module in place.
Why is it a good idea to have enough memory in your computer?

## Slide 14: The ROM chip holds the BIOS
ROM can only be read.
ROM stores the BIOS.
The BIOS is:
  A group of small software programs that control the boot process.
  Referred to as firmware.
The BIOS provides the code that wakes up the rest of the computer.
The CMOS battery maintains the BIOS settings in memory even when the computer is powered off.
CMOS battery
BIOS chip

## Slide 15: CMOS holds data after the system is turned off
Computers store configuration information in CMOS.
You change the CMOS data through the setup program.
A battery enables the CMOS to hold data when computer power is off.
If the battery is removed, setup information is lost.
Can you think of any reasons to remove the CMOS battery?

## Slide 16: POST performs diagnostic routines
Counts and checks memory
Initializes the processor and other components
Scans the hardware for firmware
Yields to firmware in other devices
Reads CMOS data and takes inventory of all components
Tests all components and reports any problems
POST Audio Signals | Probable Cause
No beep | Power supply failed or disconnected
Continuous beeping | Power supply failed or keyboard key stuck
Repeated short beeps | Power supply failed
1 long beep, 1 short beep | Motherboard failed
1 long beep, 2 short beeps | Display adapter or cable failed or missing
1 short beep, no boot | Diskette drive adapter failed
2 short beeps | Configuration error

## Slide 17: The startup routine is called the boot process
When you power on the computer, the BIOS is activated.
The BIOS initiates the POST.
The BIOS loads the operating system.
The operating system loads the system files.

## Slide 18: After startup, you can use your PC
When you open an application, the application files are loaded into RAM from the hard drive.
When you save a document, data is written to your hard drive.

## Slide 19: Slots and sockets are a PC’s foundation
Slots, sockets, and other motherboard features are the foundation of a personal computer.
The motherboard brings it all together.